# OY-BRT

## Engine start

Seatbelts	Locked

Cabin doors	Closed

Parking brake	Set

Lights and pitot heat	Off

Avionics	Off

Circuitbreakers	Check

Carburator heat	Off

Fuelselector	Least full

Mixture	 Rich

Throttle	1 cm

-----------------------------------------------------------

Masterswitch	On

Fuelquantity	Check

Beacon light	On

Navigationlights	As req.

Fuelpump	On

Prime as req.	 Primer locked

-----------------------------------------------------------

Engine…………………………………….	Start

Oilpressure………………..	OK within 30 sec.

Throttle……………………….…….	1000 RPM

Fuelpump	Off

-----------------------------------------------------------

Flaps…………………………………………	Up

Avionics……………………….……………	On

Radio selector panel………………………	Set

Gyrocompas……………………………….	Set

Altimeter…………………………….……...	Set

Parking brake………………………………	Off

## Taxilight……………………………………..	On

## Taxi

Brakes…………………………………..	Check

Flight instruments……………………...	Check

Before Take off

Taxilight…………………………………….	Off

Parking brake……………………………...	Set

Fuelselector………………………	.Fullest tank

Flight controls…………………….……	Check

Trim………………………………	Check & set

Flaps……………………………..	Check & set

-----------------------------------------------------------

Throttle……………………………...	2000RPM

Magnetos….(Max 175/50)……………	Check

Carburator heat………………………..	Check

Engine instruments……………………	Check

Suction……(Min 4”/Max 6”)……………	Check

Ampér meter…………………………...	Check

Throttle……………………………...	1000RPM

-----------------------------------------------------------

Navigation aids……………………….	As req.

Departure briefing	Complete

Fuelpump	On

Landing light………………………….…….	On

Parking brake………………………………	Off

## Line up

Pitot heat	On

Transponder	Position ”Alt”

Gyrocompas	Set to runway

Compas	Check with runway

Vr…	53kts

Vx..	64kts

Vy..	76kts

Enroute climb	87kts

# Climb	.

Flaps	Up

Fuelpump	Off

Landing light	Off

Altimeter..(If above T.A.)	Set

### Cruise

Throttle	Set

Mixture	Set

Gyrocompas	Check

Fuelselector	Set

# Before descend	.

Approach briefing	Complete

Fuelselector	Fullest tank

Mixture	Enrichen as req.

Gyrocompas	Check

VFR

Approach speed.	75kts

Threshold speed with full flaps	66kts

IFR

Holding speed	100kts

Beacon outbound	90kts

Beacon inbound	90kts

Before landing	.

Landing light…..	Consider

Altimeter	Check

Gyrocompas	Check

-----------------------------------------------------------

Fuelpump	On

Mixture	Rich

Carburator heat	On

Flaps	Set

After landing	.

Flaps	Up

Carburator heat	Off

Fuelpump	Off

Pitot heat	Off

Transponder	Stby

Landing light	Off

Taxilight	On

# Parking	.

Parking brake	Set

Taxilight	Off

Avionics	Off

Mixture	Idle cut-off

Rotating beacon	Off

Magnetos	Off

Masterswitch	Off

Controls	Lock