PA28 ARROW EMERGENCY CHECKLIST

ENGINE FIRE ON GROUND

ENGINE NOT YET RUNNING

1. STARTER....................................................ENGAGE

2. MIXTURE .........................................IDLE CUT OFF

3. THROTTLE.......................................................OPEN

CONTINUE WITH “ON GROUND EMERGENCY

CHECK LIST”

ENGINE IS RUNNING

1. FUEL SELECTOR...............................................OFF

2. THROTTLE.......................................................OPEN

WHEN FIRE STOPS CONTINUE WITH “ ON GROUND

EMERGENCY CHECK LIST”

ON GROUND EMERGENCY

1. FUEL SELECTOR...............................................OFF

2. MIXTURE .........................................IDLE CUT OFF

3. BATTERY/ALTERNATOR...................................OFF

4. MAGNETOES......................................................OFF

5. PARKING BRAKE ................................................ON

6. EVACUATE AIRCRAFT

7. IF FIRE .................................................EXTINGUISH

ENGINE FAILURE

DURING TAKEOFF RUN

1. THROTTLE..................................................CLOSED

2. BRAKES................................................SUFFICIENT

IMMEDIATELY AFTER TAKE-OFF

1. SPEED...........................................................79 KTS

2. GEAR…………………………………………….DOWN

3. FLAPS...............................................AS REQUIRED

FLY THE AIRCRAFT

DURING CRUISE

1. FUEL SELECTOR...........................CHANGE TANK

2. STBY FUEL PUMP...............................................ON

3. SPEED...........................................................79 KTS

4. ALTERNATE AIR……...........................................ON

5. MIXTURE...........................................................RICH

6. MAGNETOS.....................................................CHKD

IF NOT RESTORED, CONTINUE WITH FORCED LANDING CHECK LIST

ENGINE FIRE IN FLIGHT

1. FUEL SELECTOR...............................................OFF

2. FUEL PUMP........................................................OFF

3. THROTTLE.......................................................OPEN

4. HEATER AND DEFROSTER..............................OFF

WHEN FIRE STOPS

5. MIXTURE..........................................IDLE CUT OFF

CONTINUE WITH FORCED LANDING CHECK LIST

FORCED LANDINGS

EMERGENCY LANDING WITHOUT ENGINE POWER

1. FUEL SELECTOR...............................................OFF

2. MIXTURE .........................................IDLE CUT OFF

3. GEAR…………………………………………….DOWN

4. BATTERY/ALTERNATOR...................................OFF

5. MAGNETOS........................................................OFF

6. SEAT BELTS..............................................TIGHTEN

ELECTRICAL FAILURE

ALT ANNUNCIATOR LIGHT ILLUMINATED

1. AMMETER.................................CHECK TO VERIFY

2. IF ZERO...............................ALTERNATOR TO OFF

3. REDUCE ELECTRICAL LOADS TO MINIMUM.

4. CIRCUIT BREAKERS.....................................RESET

5. ALTERNATOR......................................................ON

6. IF NOT RESTORED..................ALTERNATOR OFF

7. THE BATTERY IS NOW THE ONLY SOURCE

ELECTRICAL FIRE IN FLIGHT

1. BATTERY/ALTERNATOR...................................OFF

2. ALL OTHER SWITCHES.....................................OFF

3. VENTS..............................................................OPEN

4. CABIN HEAT.......................................................OFF

EXTINGUISH THE FIRE. AS A LAST RESORT USE THE FIRE EXTINGUISHER. VENTILATE AFTERWARDS AND LAND AS SOON AS POSSIBLE.

IF POWER IS NECESSARY FOR COMPLETION

1. BATTERY MASTER..............................................ON

2. CIRCUIT BREAKERS…...................................CHKD

NOW TURN ON NECESSARY EQUIPMENT ONLY, ONE AT THE TIME, WITH DELAY AFTER EACH

CABIN FIRE

1. BATTERY/ALTERNATOR...................................OFF

2. VENTS/CABIN HEAT..................................CLOSED

EXTINGUISH THE FIRE. AS A LAST RESORT USE THE FIRE EXTINGUISHER. VENTILATE AFTERWARDS AND LAND AS SOON AS PRACTICAL.

MANUAL EXTENSION OF LANDING GEAR

1. CIRCUIT BREAKERS………………………..….CHKD

2. BATTERY SWICH…………………………………..ON

3. ALTERNATOR…………………………………...CHKD

4. PANEL LIGHTS…………………………………….OFF

5. NAV LIGHTS………………………………………..OFF

6. AIRSPEED……………………………….MAX 87 KTS

7. GEAR HANDLE…………………………………DOWN

8. EMERGENCY GEAR LEVER…………………DOWN

9. CHECK FOR………………………3 GREEN LIGHTS

IF GEAR STILL NOT DOWN AND LOCKED YAW

FROM SIDE TO SIDE, CONTINUE BELOW

GEAR UP EMERGENCY LANDING

1. APPROACH WITH POWER USING NORMAL SPEED

2. FLAPS…………………………………….AS DESIRED

3. THROTTLE……………………………………...CLOSE

4. BATTERY/ALTERNATOR…………………………OFF

5. IGNITION SWICH…………………………………..OFF

6. FUEL SELECTOR………………………………….OFF

7. MIXTURE….......................................IDLE CUT OFF

8. SEAT BELTS…………………………………TIGHTEN

PROPELLER OVERSPEED

1. THROTTLE…………………………………....RETARD

2. OIL PRESSURE………………………………….CHKD

3. PRP CONTROL…………………………….LOW RPM

SET PROP CONTROL IF ANY AVALIBLE.

REDUCE SPEED AND THROTTLE TO MAINTAIN MAX

2700 RPM. IF NO PWR AVALIBLE CONTINUE WITH FORCED LANDING CHECKLIST.