## BEFORE STARTING

1. COM & NAV EQUIP/TX	ON/STBY

2. ATIS	RECIEVED

3. ALTIMETERS	SET

CHECK LIST COMPLETED

BEFORE TAKE-OFF

1. ATC CLEARENCE	OBTAIN

2. NAV AIDS & TRANSPONDER	CHKD & SET

3. MIXTURES	RICH

4. PROPELLER’S	FINE PITCH

5. FUEL PUMP’S	ON

6. DEPARTURE BRIEFING	PERPORM

CHECK LIST COMPLETED

## LINE UP

1. PITOT HEAT	ON

2. LANDING & STROBE LIGHTS	ON

2. TRANSPONDER	ALT

3. GYROCOMPAS	RWY HEADING

CHECK LIST COMPLETED

VMC…	73kts

VX..	79kts

VYSE..	92kts

VAPP 25°	100kts

VTH 40°	80kts

# CLIMB	.

1. GEAR	UP

2. FLAPS	UP

3. CLIMB POWER (25/2500)	SET

4. COWL FLAPS	SET

5. LANDING LIGHT	OFF

6. FUEL PUMP	OFF

7. ALTIMETER (IF ABOVE T.A.)	SET

CHECK LIST COMPLETED

### CRUISE

1. POWER	SET

2. COWL FLAPS	CLOSED

3. MIXTURE	SET

4. DIRECTIONAL GYRO	CHKD

CHECK LIST COMPLETED

# DESCENT	.

1. MIXTURES	SET

2. DIRECTIONAL GYRO	SET

3. FUEL SELECTORS	TANK TO ENGINES

4. APPROACH BRIEFING	COMPLETE

CHECK LIST COMPLETED

APPROACH	.

1. ALTIMETER…..	HPA SET

2. DIRECTIONAL GYRO	SET

3. FUEL PUMP’S	ON

4. MIXTURE’S	RICH

5. PROPELLER’S	2500 RPM

6. NAV AIDS	SET & CHKD

------------------------------------------------------------------

7. PROPELLER’S	FINE PITCH

8. GEAR	DOWN & CHKD

9. LANDING LIGHTS	ON

CHECK LIST COMPLETED

GO AROUND	.

AFTER A GO AROUND / TAKE OFF DIRECTLY

FOLLOWED BY AN APPROACH WITHOUT

FLIGHT ABOVE TRANSITION ALT.

1. GEAR…..	UP

2. FLAPS	UP

3. CLIMB POWER (25/2500)	SET

4. DIRECTIONAL GYRO	CHKD

5. COWL FLAPS	SET

6. LANDING LIGHTS	OFF

7. NAV AIDS	SET & CHKD

------------------------------------------------------------------

7. PROPELLER’S	FINE PITCH

8. GEAR	DOWN & CHKD

9. LANDING LIGHTS	ON

CHECK LIST COMPLETED

# AFTER LANDING	.

1. FLAPS	UP

2. COWL FLAPS	OPEN

3. ICE PROTECTION	OFF

4. PITOT HEAT	OFF

5. FUEL PUMPS	OFF

6. TRANSPONDER	STANDBY

CHECK LIST COMPLETED

# PARKING	.

1. PARKING BREAK	ON

2. TAXI LIGHT	OFF

3. RADIOS/NAV EQUIPMENT	OFF

4. THROTTLE	1000 RPM

5. MIXTURE’S	IDLE CUT-OFF

6. LIGHTS	OFF

7. MASTER / ALTERNATOR	OFF

8. MAGNETO’S	OFF

9. TRIM	RESET

CHECK LIST COMPLETED

1. CONTROLS	LOCKED

2. AIRCRAFT	SECURED

# Text boxes

PA34-200 SHORT SIMULATOR CHECKLIST